## Slide 1
NORSK DATA · ND-100 / ND-110 / ND-120
The NORD-100 Bus
One shared path ties the CPU, memory, and every I/O device together. This deck walks the bus phase by phase — signals, arbitration, register access, interrupts, identification, and direct memory access — each with its real timing and the original manual's own words.
Text quoted verbatim from ND-06.016.01 NORD-100 Input/Output System and ND-06.015.02 Functional Description. Timing diagrams reconstructed from the manual figures and validated against the ND-120 RTL.

## Slide 2
OVERVIEW · SECTION I
Four kinds of agent, one bus
In the NORD-100, every hardware module hangs off one common bus. Only one agent uses it at a time; the Bus Control Unit decides whose turn it is.
RUNS PROGRAMS
CPU
fetch, store, service interrupts
MOVES DATA
I/O device controllers
disk, tape, terminal, printer
HOLDS DATA
Memory
the shared store
THE NORD-100 BUS — 24-bit multiplexed address/data + control + interrupt lines
REFEREE
Bus Control Unit (BCU)
on the CPU module — grants each cycle to the CPU, a DMA device, or refresh
FROM THE MANUAL
“In the NORD-100 computer system all hardware modules are connected together via a common bus, the NORD-100 bus… the NORD-100 bus is general purpose, to allow all classes of NORD-100 modules simply to be ‘plugged’ into the system.”
ND-06.016.01 · I.2.1, p. I-2-1
“The NORD-100 CPU uses the bus for memory transfers… In addition, some NORD-100 bus peripherals (DMA controllers) can initiate transfers directly to and from the memory system.”
II.1, p. II-1-1
“Each NORD-100 bus backplane position contains a total of 96 lines… All positions in the backplane contain the same information, i.e., they are equal.”
I.2, p. I-2-5

## Slide 3
CONVENTIONS · APPENDIX F
The lines, and how to read them
One 24-bit multiplexed address/data bus (BD0–23) plus named control lines. Every logic signal is active low; many are wired-OR (any slot may pull them).
Address / data
BD0–23 — multiplexed; address in the address cycle, word in the data cycle. BD0 = LSB.
Cycle strobes
BAPR · BDAP · BDRY · BIOXE · BINPUT · BINACK
Control
BREQ · BMEM · BMCL · BERROR · BPERR
Interrupt
BINT10 · BINT11 · BINT12 · BINT13 · BINT15 (BINT10 lowest priority)
Daisy chains
INGRANT→OUTGRANT · INIDENT→OUTIDENT (priority tokens, slot to slot)
FROM THE MANUAL
“All logic signals are in the active low polarity, i.e.: Logical ‘0’ — 2.4 to 5.0 volts; Logical ‘1’ — 0 to 0.5 volts.”
Appendix F, p. F-1
“BREQ — Request for a DMA cycle. Wired OR line. · BAPR — Bus Address Present… Wired OR line. · BDRY — Bus Data Ready… given by answering device. Wired OR line. · BDAP — Bus Data Present… during DMA or memory cycles. · BMEM — Bus Memory Cycle… Generated by controlling unit. · BINT10-13, 15 — Interrupt lines. BINT10 has lowest priority. Wired OR lines.”
Appendix F.2, pp. F-3 … F-6

## Slide 4
THE BUS · SECTION II.2
Three things want the bus
The bus must be allocated before use, is busy to everyone else while held, and is released after one word. Three requestors compete.
REASON 1–6
CPU — fetch / read / store / IOX / control-reg
BREQ
DMA controllers — need a word from, or have a word for, memory
RFREQ · EVERY 15 ΜS
Memory refresh — dataless cycle to keep DRAM alive
FROM THE MANUAL
“As a common resource, the NORD-100 bus has to be allocated before it may be used. Once allocated, the bus is busy to other activities, while the granted bus user may transfer one word. As the transfer is completed the NORD-100 bus should be released for next eventually requesting bus user.”
II.2, p. II-2-1
“The NORD-100 CPU may request access… for one of six reasons: instruction fetch / operand read / indirect address read / operand store; programmed access to the I/O system; programmed access to external system control registers.”
II.4.1.1.1, p. II-4-2

## Slide 5
THE BUS · SECTION II.3 / II.5
One bus cycle = allocate → transfer → release
Exchanging one word is a bus cycle. Because address and data share the same lines, the transfer splits into an address subcycle then a data subcycle.
Allocate (BCU grants)
→
Transfer one word
→
Terminate & release
Address cycle — BAPR + address on BD
→
Data cycle — handshake: BDAP → BDRY
FROM THE MANUAL
“A NORD-100 bus cycle consists of three main events: allocation of a requesting bus user; transfer one word; termination and release of the bus… The transfer and termination of a bus cycle is organized as a handshake between the selected bus user (CPU, DMA or refresh) and it's accessed device. The concept allows completely asynchronously operation within a bus cycle.”
II.3, p. II-3-1
“Due to the multiplexing of addresses and data on the same physical bus lines, one NORD-100 bus cycle may be divided up into two subcycles: first, an address cycle; second, a data cycle. The Address cycle precedes the data cycle.”
II.5.1, p. II-5-1

## Slide 6
THE BUS · SECTION II.4
Arbitration: who gets the next cycle
The BCU's priority arbiter picks one requestor per cycle. Refresh outranks DMA; between DMA and CPU, priority toggles. Among DMA devices, a daisy-chained token sets order.
NOTE
“Already allocated bus is not interruptable. The bus cycle going on is aborted if it exceeds 8 µs. If the bus is idle and an allocation request appears alone: first come, first served. RFREQ and BREQ are both handled as DMA requests but RFREQ is given highest priority. If both DMA and CPU requests are present, priority is given to the one not having the previous cycle (toggled priority).”
II.4.1.2, p. II-4-4
BCU / CPU
OUTGRANT →
→
slot 1
no BREQ — passes
→
slot 2 ✓
GRANTED — stops chain
→
slot 3
never reached
FROM THE MANUAL
“When there are several DMA controllers, each controller's request signal is ‘wired or’ to one bus allocation request line… the DMA request acknowledge signal is daisy chained in the NORD-100 bus backplane. The daisy chain then establishes a sequential priority scheme between DMA controllers.”
II.4.1.1.2, p. II-4-3
“INGRANT — An interface which issued BREQ prior to the last leading edge of BMEM may use the bus for a single memory read or write cycle. Otherwise, INGRANT is passed onto OUTGRANT… of the next lower priority card position.”
Appendix F.2, p. F-4

## Slide 7
PROGRAMMED I/O · SECTION III
IOX — the CPU reads & writes a device register
The only instructions for talking to an interface are IOX / IOXT. Present the register address (LSB picks direction), open the IOX window, take or hand over a word.
IOX WRITE CPU → reg 1563 ← 000004
BAPR
BIOXE
acc
BAPR_n
addr+dir
BIOXE_n
window
BDRY_n
accepted
BD[23:0]
master
1563
000004
iox_wr
strobe
IOX READ CPU ← reg 1562 → 004010
BAPR
BINPUT/ACK
data
rel
BAPR_n
addr+dir
BIOXE_n
window
BINPUT_n
have data
BINACK_n
CPU ready
BDRY_n
ready
BD[23:0]
device
1562
004010
iox_rd
strobe
FROM THE MANUAL
“In the address cycle, all I/O interfaces, simultaneously, are presented the device register address. Based on this address, one I/O device register is selected to communicate with the CPU during the data cycle.”
III.2.4, p. III-2-7
Write: “when the data (the A register) is valid on the BD lines, the handshake logic activates BIOXE₀… The interface that finds equal address strobes the content of the BD lines into the specified device register… then activates BDRY₀ to signify ‘data accepted’.”
III.2.4 Case 1, p. III-2-8
Read: “the interface activates BINPUT₀… BINACK means that the BD lines are free to accept data… the interface enables the accessed input register onto the BD lines… generates the BDRY₀ signal.”
III.2.4 Case 2, p. III-2-9

## Slide 8
INTERRUPT SYSTEM · SECTION I.4
Interrupts: 16 levels, four on the bus
16 program levels; the highest active one runs. Levels 10–13 are hardware interrupt lines in the bus, each shared by a class of device. Level 14 is internal traps.
Level | Line | Used by
13 | BINT13 | Real-time clock(s), special-attention devices
12 | BINT12 | Input channel of all PIO interfaces
11 | BINT11 | All DMA controllers (mass storage)
10 | BINT10 | Output channel of all PIO (lowest priority)
14 | — | Internal CPU traps (MOR, IOX err, parity, power)
15 | BINT15 | Not used by ND — users needing immediate access
FROM THE MANUAL
“The NORD-100 interrupt system consists of 16 program levels… numbered from 0 - 15 with increasing priority; program level 15 has highest priority, program level 0 lowest. At any time, the highest active level is running.”
I.4.2, p. I-4-2
“Level 10 is used by the output channel of all PIO interfaces; Level 11 is used by all DMA controllers; Level 12 is used by the input channel of all PIO interfaces; Level 13 is used by the real-time clock(s)…”
I.4.4, p. I-4-7
“The control of the NORD-100 priority interrupt system is based on two registers: the Priority Interrupt Enable register (PIE); the Priority Interrupt Detect register (PID).”
I.4.2, p. I-4-2

## Slide 9
IDENTIFICATION · SECTION IV
IDENT — which device interrupted?
Levels 10–13 are shared, so a raised BINT doesn't say who. IDENT PLxx searches one level; the first device (by daisy priority) returns its ident code and clears its interrupt.
IDENT — device replies (level 11, ident 021)
BAPR 011
poll
drive 021
ACK
clr
BINT11_n
our int
BAPR_n
poll code
OUTIDENT_n
poll
GRANT_IN
token
GRANT_OUT
consumed
BINPUT_n
have data
BDRY_n
code ready
BD[23:0]
in/out
011
021
FROM THE MANUAL
“In the IDENT address cycle, the level on which the interrupt search is to be performed, is presented on the BD lines, combined with BAPR₀. All I/O interfaces having interrupt on the specified level turn on a ‘flag’.”
IV.2.2, p. IV-2-4
“If the BINIDENT signal reaches a module with the ‘flag’ set, the search is stopped. The interface that stopped the search returns its ident code to the CPU, combined with BDRY₀. Modules with no interrupt ‘flag’ set should… pass BINIDENT further to the next slot position.”
IV.2 ‘Interrupt Handling Logic’, p. IV-2-6
“INIDENT — Response to BINT10-13, together with address bits 0-5 which specify BINT number…”
Appendix F.2, p. F-4

## Slide 10
IDENTIFICATION · DETAIL
Poll code ≠ level number
The value strobed at BAPR is a poll code in address bits 0–5 — not the level as an integer. The device answers with a separate ident code. Up to 2048 vectors (512 × 4 levels).
Level | Poll (oct) | Devices → ident (oct)
10 | 004 | PIO output · line printer 03
11 | 011 | floppy DMA 021 · SMD 017
12 | 022 | PIO input · papertape 02 · terminal 01
13 | 043 | real-time clock
Only level 11 resembles its own number (011₈). 10→004, 12→022, 13→043 clearly do not.
FROM THE MANUAL
“Each I/O device controller is assigned an interrupt vector referred to as ‘ident code’… There is a unique correspondence between an external device, the device number and the ident code. On the interfaces, the ident code… is selectable by a thumbwheel.”
I.4.5.2, p. I-4-9
“In ND-100 there may be up to 2048 vectored interrupts… The first interrupting device found will respond with its 9 bit identification code and reset its interrupt condition… 9 bits give 512 different vectors on each of the four actual levels.”
ND-06.015.02 · 2.9.2.3.1, p. 2-68

## Slide 11
DIRECT MEMORY ACCESS · SECTION V
DMA — a device moves data itself
A granted DMA controller runs an ordinary memory cycle with no CPU help: address (BAPR) → data phase (BDAP) → memory answers BDRY. The BCU only watches the 8 µs timeout.
DMA READ memory 010000 → device
IDLE
REQ
ADDR
DATA
END
gap
BREQ_n
request
BMEM_n
bus-mem
INGRANT_n
token
BAPR_n
addr
BINPUT_n
high=read
BDAP_n
data
BDRY_n
ready
BD[23:0]
addr/data
010000
042525
dma_ack
done
DMA WRITE device → memory 010000
IDLE
REQ
ADDR
DATA
END
gap
BREQ_n
request
BMEM_n
bus-mem
INGRANT_n
token
BAPR_n
addr
BINPUT_n
LOW=write
BDAP_n
data
BDRY_n
accepted
BD[23:0]
master
010000
042525
dma_ack
done
FROM THE MANUAL
“As the request is granted the BCU issues BMEM… It enables the memory system… and ‘freezes’ the DMA request status… leading edge of BMEM₀ is the last chance for a DMA request to be served by the current INGRANT/OUTGRANT search.”
V.4, p. V-4-2
Read: “BINPUT not active tells the memory system that the started reference is a read… BDAP₀… means memory may enable data to the BD lines… memory activates BDRY₀. The DMA controller uses BDRY₀ to strobe the read data into a data buffer.”
V.4 Case 1, p. V-4-2
Write: “BINPUT true informs the memory system that the… cycle is a write… the DMA controller combines the data with BDAP₀. The memory system uses BDAP₀ to strobe the data… and activates BDRY₀ to signify ‘data accepted’.”
V.4 Case 2, p. V-4-3

## Slide 12
DMA · SECTION I.3.7 / V.5
One word per grant — and a rest between
Set up by IOX (address, block, word-count registers), then a block transfers one word per grant, re-requesting each time — until the word counter hits zero and it interrupts on level 11.
Re-request cadence (manual II.4 examples ≈ 1.4–6 µs apart), to scale:
recovery gap
recovery gap
Registers (I.3.7.1): Memory Address (MAR), Block Address (BAR), Word Count, Control (bit 2 = start). Each grant: MAR+1→MAR, WC−1→WC, loop until WC=0.
FROM THE MANUAL
“The first module found with DMA request set is granted and is allowed to make a one word exchange. Thus, the INGRANT/OUTGRANT daisy chain establishes a sequential priority scheme between the DMA controllers.”
V.3, p. V-3-1
“Data is exchanged between the DMA controller and memory at the speed determined by the device. CPU may run any activity not waiting for the DMA transfer to be completed.”
I.3.7, p. I-3-30
“The DMA transfer is completed when the word counter is zero… status register bit 3 (ready for transfer) is turned on… this causes interrupt on level 11.”
I.3.7, p. I-3-31
“the BCU is not involved in the memory reference… the only control signal in response from the memory system is BDRY₀.”
V.5, p. V-5-1

## Slide 13
ERRORS · II.4.2 + FUNCTIONAL DESCRIPTION
When a cycle goes wrong
If the accessed device never returns BDRY, the BCU's 8 µs timer aborts the cycle and raises an internal interrupt on level 14. The internal interrupt code (IIC) says why.
allocate → 8 µs timer
→
no BDRY
→
abort + release
→
level-14 interrupt
IIC (oct) | Cause
7 | IOX error — no answer from external device
10 | Memory parity error (PTY)
11 | Memory out of range (MOR)
12 | Power fail (POW) — has priority
FROM THE MANUAL
“One bus cycle should not last for more than 8 µs. This is monitored by the BCU… a bus cycle that exceeds 8 µs is aborted by the BCU timeout timer. The faulty cycle is reported to the CPU as an internal interrupt (level 14).”
II.4.2, p. II-4-6
“IOX 7 — IOX error. No answer from external device. PTY 10 — Memory parity error. MOR 11 — Memory out of range. POW 12 — Power fail interrupt.”
ND-06.015.02 · p. 2-70
“If a MOR occurs during a DMA cycle this will be indicated in the PES… by bit 14 (DMA) set and bit 15 (Fetch) not set.”
V.5, p. V-5-1

## Slide 14
BEYOND ONE CRATE · SECTION VI
The Bus Extender — chaining crates
One crate holds 12 or 21 slots. To go further, up to 8 crates are linked by Bus Extender (BEX) modules. The daisy chains must stay unbroken — the master BEX sits right after the last device in the CPU crate.
Crate A
CPU + master BEX (no. 0)
→
Crate B
BEX no. 1
→
… up to H
BEX no. 7
FROM THE MANUAL
“The BEX system makes it possible to extend the NORD-100 bus structure by linking together from two to a theoretical maximum of 8 NORD-100 card crates… only one CPU module can be connected to the system.”
VI.1, p. VI-1-1
“The overall subject in the placement rules is to maintain the propagation of the daisy chained backplane signals… there should never be any empty positions between the CPU and the first BEX in the crate chain, i.e., the MASTER BEX.”
VI.2.2, p. VI-2-2
“During a memory reference… all crates will be presented the memory address simultaneously… all BEX modules, in parallel, will ‘look’ at the address to see if it is between the Lower Limit and Upper Limit set for the crate. Only one BEX should find the presented address between its limits.”
VI.3.2, pp. VI-3-2 … 3

## Slide 15
THE REST · APPENDIX F + MISC
Refresh, master clear, power, console
A few more bus phases and lines complete the picture — mostly the arbiter's housekeeping or CPU-crate-only console signals.
Refresh
Dataless memory cycle. RFREQ every 15 µs from a CPU-module oscillator, highest DMA-class priority; memory blocked while it runs.
Master clear — BMCL
Wired-OR. Initializes all logic at power-up and when the Master Clear button is pushed.
Power — BMINH / standby
Inhibits memory access during power down/up on battery-backed systems; +5V/+12V standby retain memory.
Console (CPU crate only)
LOAD, RESTART (start at 20₈), RUN, STOP, CONTINUE — operator control of CPU run state.
Future — BCRQ / INCONTR
A full-bus-control request + daisy chain ‘for future extensions’. No semaphore / locked cycle is defined in the manual.
FROM THE MANUAL
“Refresh is a periodical operation needed by the dynamic MOS memory circuits… initiated every 15 µs by an oscillator on the CPU module activating the signal RFREQ.”
II.4.1.1.3, p. II-4-3
“BMCL — Bus Master Clear for logic initialization at power up and when Master Clear button is pushed. Wired OR line. · RESTART — Starts program execution in location 20₈ if the CPU is in STOP mode.”
Appendix F.2, pp. F-3 … F-6

## Slide 16
SOURCES
Where this comes from
FROM THE MANUAL
ND-06.016.01 — NORD-100 Input/Output System: the bus (II), IOX (III), IDENT (IV), DMA (V), bus extender (VI), signal glossary (App. F).
ND-06.015.02 — ND-100 Functional Description: the interrupt system, internal-interrupt codes, the 9-bit / 2048-vector detail.
NOTE
The waveforms are reconstructions of the manual's figures (II.5.1, III.2.4/5, IV.2.3, V.4.1/2, V.5.1) — those figures did not survive OCR — cross-checked against the repo writeup Verilog/docs/nd100-bus-dma.md and validated against the ND-120 RTL (ND_BUS_SLAVE.v, ND_DMA_MASTER.v, PAL_44801A.v). Level usage is taken from the manual text (I.4.4), not the one OCR figure whose table was scrambled.